## Slide 1: eK9 Smart Metal Detector
Paulius Miliunas
Software and Electronics Engineering

## Slide 2: eK9 Block Diagram

## Slide 3: Detector Hardware
Metal Detecting circuit uses 555 timer and 2 op-amps. U2 op-amp is used as smith trigger, and U3 op-amp is used as buffer for converting logic voltages for esp32.

## Slide 4: Prototype Build
Prototyped board runs of 5v
Have voltage regulator to power up MCU
When running uses 500mA

## Slide 5: The Brain of eK9
MCU configured to detect falling edge of signal and on interrupt take time stamp
MCU calculates frequency and sends vie Bluetooth to smartphone

## Slide 6: eK9 enclosure
All system build in one frame
Smart Phone can be attached to enclosure
Rechargeable battery attached with battery protection circuit

## Slide 7: eK9 Comms App
Bluetooth communication
App running on android can receive data from eK9 device
App will be notified about frequency change and react as instructed.

## Slide 8: Thank You
Any questions